libiotrace
JSON_STRUCT macros

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
json_structs.h includes
json_defines.h
Activates defines to generate
structures in json_defines.h
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
json_structs.h
JSON_STRUCT_START(file_descriptor)
 JSON_STRUCT_INT(descriptor)
JSON_STRUCT_END
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Order of the definitions in json_structs.h is important.
A struct can only be used as a part of a other struct if it was defined before it is used.

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
JSON_STRUCT_START(file_descriptor)
 JSON_STRUCT_INT(descriptor)
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 JSON_STRUCT_INT(descriptor)
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 JSON_STRUCT_INT(descriptor)
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 JSON_STRUCT_SIZE_T(length)
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Pointer to other struct and enum to store
information which other struct is stored in
pointer

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Each enum value represents one
struct which can be stored in
pointer

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   void_p_enum_file_type_file_memory,
 JSON_STRUCT_VOID_P_END(file_type)
Each enum value has a unique name
build from a prefix followed by the
pointer name and the name of the
referenced structure

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   void_p_enum_file_type_file_memory,
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   void_p_enum_file_type_file_memory,
 } void_p_enum_file_type;
Enum has a unique name
build from a prefix followed
by the pointer name

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   void_p_enum_file_type_file_memory,
 } void_p_enum_file_type;

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   void_p_enum_file_type_file_memory,
 } void_p_enum_file_type;
};

---
#if JSON_STRUCT == JSON_STRUCT_DATA_TYPE
# define JSON_STRUCT_START(name) struct name {
# define JSON_STRUCT_END };
# define JSON_STRUCT_INT(name) int name;
# define JSON_STRUCT_VOID_P(name) void *name;
# define JSON_STRUCT_SIZE_T(name) size_t name;
# define JSON_STRUCT_PID_T(name) pid_t name;
# define JSON_STRUCT_VOID_P_START(name) \
        void *name; enum {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        void_p_enum_##name##_##element,
# define JSON_STRUCT_VOID_P_END(name) \
        } void_p_enum_##name;
struct file_descriptor {
 int descriptor;
};
struct file_memory {
 void *address;
 size_t length;
};
struct basic {
 pid_t process_id;
 void *file_type; enum {
   void_p_enum_file_type_file_descriptor,
   void_p_enum_file_type_file_memory,
 } void_p_enum_file_type;
};
Three different structures
ready to be included

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
Activates defines to generate
functions to evaluate max. size
of json-string to print
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_hasElements = 1; \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
JSON_STRUCT_START(file_descriptor)
 JSON_STRUCT_INT(descriptor)
First a simple struct with only one element

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
JSON_STRUCT_START(file_descriptor)
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
For each struct in json_structs.h a own function is generated.
The function name a prefix followed by the struct name.
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_INT(descriptor)
Variable needed to work with empty structs
(to generate empty json-objects). If set to
1 we have added 1 for a comma after the
last element and must remove it (see later
slides).

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_INT(descriptor)
Variables only needed for special structure elements are marked
with __attribute__((unused)) to inform the compiler,
so they can be ommited if the generated function doesn’t use them

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(descriptor, \
   JSON_STRUCT_TYPE_SIZE_DEC(int) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(descriptor, \
   JSON_STRUCT_TYPE_SIZE_DEC(int) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(descriptor, \
   ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
   + 1) /* for sign (-) */
Evaluates how many digits are necessary
to represent a number as a decimal

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(descriptor, \
   ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("descriptor") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("descriptor") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
Gives count of bits
for one char
e.g.:
"descriptor":-2471,

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("descriptor") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("descriptor") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 if (json_struct_hasElements) \
   json_struct_size--; /* remove last comma */ \
 json_struct_size++; /* close parentheses */ \
 return json_struct_size; \
}
e.g.:
{"descriptor":-2471}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(int) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_descriptor() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("descriptor") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(int) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 if (json_struct_hasElements) \
   json_struct_size--; /* remove last comma */ \
 json_struct_size++; /* close parentheses */ \
 return json_struct_size; \
}
Function to get the maximum bytes needed to
represent the struct file_descriptor as a json-object:
int json_struct_max_size_file_descriptor()
(all values are constants, so compiler can fold it)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)
Second a less simple struct with
two elements

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
JSON_STRUCT_START(file_memory)
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_VOID_P(address)
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(address, \
   JSON_STRUCT_TYPE_SIZE_HEX(void*) \
   + 2) /* quotation marks (for value) */
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(address, \
   JSON_STRUCT_TYPE_SIZE_HEX(void*) \
   + 2) /* quotation marks (for value) */
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(address, \
   ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
   + 2) /* quotation marks (for value) */
 JSON_STRUCT_SIZE_T(length)
Evaluates how many digits are necessary
to represent a number as a hexadecimal

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(address, \
   ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
   + 2) /* quotation marks (for value) */
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_SIZE_T(length)
e.g.:
"address":"0xA9B01",

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_SIZE_T(length)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_ELEMENT_SIZE(length, \
   JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_ELEMENT_SIZE(length, \
   JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_ELEMENT_SIZE(length, \
   ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_ELEMENT_SIZE(length, \
   ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
   + 1) /* for sign (-) */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("length") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("length") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
Second assignment of same value to same
variable will be omitted by compiler

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("length") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("length") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 if (json_struct_hasElements) \
   json_struct_size--; /* remove last comma */ \
 json_struct_size++; /* close parentheses */ \
 return json_struct_size; \
}
e.g.:
{"address":"0xA9B01","length":512}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_VOID_P(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_HEX(void*) \
        + 2) /* quotation marks (for value) */
# define JSON_STRUCT_SIZE_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, JSON_STRUCT_TYPE_SIZE_DEC(size_t) \
        + 1) /* for sign (-) */
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_HEX(type) \
        ((sizeof(type) * 2) + 2) /* +2 for "0x"-prefix */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_file_memory() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("address") \
   - 1 /* trailing null character */ \
   + ((sizeof(void*) * 2) + 2) /* +2 for "0x"-prefix */ \
     + 2 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("length") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(size_t) * CHAR_BIT))) \
     + 1 \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 if (json_struct_hasElements) \
   json_struct_size--; /* remove last comma */ \
 json_struct_size++; /* close parentheses */ \
 return json_struct_size; \
}
Function to get the maximum bytes needed to
represent the struct file_memory as a json-object:
int json_struct_max_size_file_memory()
(all values are constants, so compiler can fold it)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Third a more complex struct with two elements.
One element a simple variable. The other element
a pointer to one of two possible structs.
Defines for the pointer to the other struct are
displayed on a later slide (for better readability).

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(process_id, \
   JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
A valid pid_t (process id) can only be
positive, so no sign is needed.

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(process_id, \
   JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(process_id, \
   ceil(log10(pow(2, sizeof(pid_t) * CHAR_BIT))))
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 JSON_STRUCT_ELEMENT_SIZE(process_id, \
   ceil(log10(pow(2, sizeof(pid_t) * CHAR_BIT))))
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("process_id") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(pid_t) * CHAR_BIT))) \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("process_id") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(pid_t) * CHAR_BIT))) \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
The pointer to a other struct needs additional defines displayed
on a later slide, so first we look at the last part of the new function.

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_START(name) \
       int json_struct_max_size_##name() { \
        char json_struct_hasElements = 0; \
        __attribute__((unused)) int json_struct_size_void_p; \
        __attribute__((unused)) int json_struct_size_void_p_tmp; \
        size_t json_struct_size = 1; /* open parentheses */
# define JSON_STRUCT_END \
        if (json_struct_hasElements) \
        json_struct_size--; /* remove last comma */ \
        json_struct_size++; /* close parentheses */ \
        return json_struct_size;}
# define JSON_STRUCT_PID_T(name) \
        JSON_STRUCT_ELEMENT_SIZE(name, \
        JSON_STRUCT_TYPE_SIZE_DEC(pid_t))
# define JSON_STRUCT_ELEMENT_SIZE(name, sizeValue) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + sizeValue \
        + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
# define JSON_STRUCT_TYPE_SIZE_DEC(type) \
        ceil(log10(pow(2, sizeof(type) * CHAR_BIT)))
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("process_id") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(pid_t) * CHAR_BIT))) \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 if (json_struct_hasElements) \
   json_struct_size--; /* remove last comma */ \
 json_struct_size++; /* close parentheses */ \
return json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
Now we need the up to now unused variables
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("process_id") \
   - 1 /* trailing null character */ \
   + ceil(log10(pow(2, sizeof(pid_t) * CHAR_BIT))) \
   + 4; /* quotation marks (for key),*/ \
        /* colon and comma */
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 if (json_struct_hasElements) \
   json_struct_size--; /* remove last comma */ \
 json_struct_size++; /* close parentheses */ \
return json_struct_size;}
Defines for pointer to other structure

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
We ommit known parts to get more space
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}
We ommit known parts to get more space

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}
Length of name of json object inside the json object.
e.g. (in red):
{"process_id":"1005","file_type":{…},...}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}
Maximum length of pointed to structure, initialized to 0

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}
Magic at work: to get the maximum length of a pointed to structure we can use the already
generated function for this structure. Thats because structures can only be elements in other
structures if they are defined before and the definition of all structures in json_structs.h is
transformed by macros to a function.

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}
Check if the maximum length of the pointed to structure is larger than the last one
(it is, because it’s the first of two possible structures and therefore the size is initialized to 0)
and keep the bigger value. We use the same macro for each possible structure, so for the
first one there is an unnecessary if-statement (it will be optimized away by the compiler).

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_memory(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}
Now we use the function for the other struct to get the maximum length for this struct as json
and keep the greater of the two lengths.

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_memory(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 JSON_STRUCT_VOID_P_END(file_type)
 {...}
return json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_memory(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 json_struct_size += json_struct_size_void_p;
 {...}
return json_struct_size;}
Add the length of the biggest struct that can be
pointed to to the length that will be returned.

---
#if JSON_STRUCT == JSON_STRUCT_BYTES_COUNT
# define JSON_STRUCT_VOID_P_START(name) \
        json_struct_size += sizeof(#name) \
        - 1 /* trailing null character */ \
        + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
        json_struct_size_void_p = 0;
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        json_struct_size_void_p_tmp = \
        json_struct_max_size_##element(); \
        if(json_struct_size_void_p_tmp > \
        json_struct_size_void_p) \
        json_struct_size_void_p = \
        json_struct_size_void_p_tmp;
# define JSON_STRUCT_VOID_P_END(name) \
        json_struct_size += \
        json_struct_size_void_p;
int json_struct_max_size_basic() { \
  char json_struct_hasElements = 0; \
  __attribute__((unused)) int json_struct_size_void_p; \
  __attribute__((unused)) int json_struct_size_void_p_tmp; \
  size_t json_struct_size = 1; /* open parentheses */
 json_struct_hasElements = 1; \
 json_struct_size += {...};
 json_struct_hasElements = 1; \
 json_struct_size += sizeof("file_type") \
   - 1 /* trailing null character */ \
   + 4; /* quotation marks (for key), */ \
        /* colon and comma */ \
 json_struct_size_void_p = 0;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_descriptor(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 json_struct_size_void_p_tmp = \
   json_struct_max_size_file_memory(); \
 if(json_struct_size_void_p_tmp > json_struct_size_void_p) \
   json_struct_size_void_p = json_struct_size_void_p_tmp;
 json_struct_size += json_struct_size_void_p;
 {...}
return json_struct_size;}
Function to get the maximum bytes needed to
represent the struct basic as a json-object:
int json_struct_max_size_basic()
(all values are constants, so compiler can fold it)
Includes the maximum of
int json_struct_max_size_file_descriptor() and
int json_struct_max_size_file_memory()
(the two structures which can be part of struct basic)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
Activates defines to generate
functions to print json-string
to a buffer
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
JSON_STRUCT_START(file_descriptor)
 JSON_STRUCT_INT(descriptor)
First a simple struct with only one element
First only defines for start and end part of function
Macro to call real fprintf function and not a wrapper (if one is present)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
JSON_STRUCT_START(file_descriptor)
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 JSON_STRUCT_WRITE("{")
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 JSON_STRUCT_WRITE("{")
 JSON_STRUCT_INT(descriptor)
1. argument: pointer to the first byte of the buffer to print the json to
2. argument: lenght of the buffer
3.argument: struct to print

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 JSON_STRUCT_WRITE("{")
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
   json_struct_size) \
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)
Function to write max. json_struct_size Bytes to buffer json_struct_buf.
Longer strings will be shortened and terminated with "\0".

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
   json_struct_size) \
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)
Buffer filled with e.g.: "{" (of course terminated by \0)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
   json_struct_size) \
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 if (json_struct_ret >= json_struct_size) { \
   CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
     "Output buffer in function %s not big enough.\n", \
     __func__); \
   assert(0); \
 }
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 if (json_struct_ret >= json_struct_size) { \
   CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
     "Output buffer in function %s not big enough.\n", \
     __func__); \
   assert(0); \
 }
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 if (json_struct_ret >= json_struct_size) { \
   CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
     "Output buffer in function %s not big enough.\n", \
     __func__); \
   assert(0); \
 }
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)
 if (json_struct_hasElements) { \
   json_struct_buf--; /* remove last comma */ \
   json_struct_size++; /* and resize buffer size */ \
 } \
 JSON_STRUCT_WRITE("}") \
 return json_struct_start_size - json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 if (json_struct_ret >= json_struct_size) { \
   CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
     "Output buffer in function %s not big enough.\n", \
     __func__); \
   assert(0); \
 }
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)
 if (json_struct_hasElements) { \
   json_struct_buf--; /* remove last comma */ \
   json_struct_size++; /* and resize buffer size */ \
 } \
 JSON_STRUCT_WRITE("}") \
 return json_struct_start_size - json_struct_size;}
Same as a few slides before. We omit it.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_START(name) \
       int json_struct_print_##name(char* json_struct_buf, \
        size_t json_struct_size, \
        struct name *json_struct_data) { \
        char json_struct_hasElements = 0; \
        int json_struct_ret = 0; \
        int json_struct_start_size = json_struct_size; \
        JSON_STRUCT_WRITE("{")
# define JSON_STRUCT_END \
        if (json_struct_hasElements) { \
        json_struct_buf--; /* remove last comma */ \
        json_struct_size++; /* and resize buffer size */ \
        } \
        JSON_STRUCT_WRITE("}") \
        return json_struct_start_size - json_struct_size;}
# define JSON_STRUCT_WRITE(value) \
        json_struct_ret = json_struct_write(json_struct_buf, \
        json_struct_size, value); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 json_struct_ret = json_struct_write(json_struct_buf, \
   json_struct_size, "{"); \
 if (json_struct_ret >= json_struct_size) { \
   CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
     "Output buffer in function %s not big enough.\n", \
     __func__); \
   assert(0); \
 }
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 JSON_STRUCT_INT(descriptor)
 if (json_struct_hasElements) { \
   json_struct_buf--; /* remove last comma */ \
   json_struct_size++; /* and resize buffer size */ \
 } \
 JSON_STRUCT_WRITE("}") \
 return json_struct_start_size - json_struct_size;}
Buffer filled with e.g.: "{...}" (of course terminated by \0)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 JSON_STRUCT_INT(descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}
We ommit known parts to get more space
Needed definitions for JSON_STRUCT_INT

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 JSON_STRUCT_INT(descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 JSON_STRUCT_ELEMENT(descriptor, %d, \
   json_struct_data->descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 JSON_STRUCT_ELEMENT(descriptor, %d, \
   json_struct_data->descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 JSON_STRUCT_SNPRINTF( \
   JSON_STRUCT_QUOT(descriptor)":""%d"",", \
   json_struct_data->descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}
Because of ellipses (…) and use of __VA_ARGS_, macro could become multiple arguments.
Argument count and type must fetch the template placeholders (see printf function).

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 JSON_STRUCT_SNPRINTF( \
   JSON_STRUCT_QUOT(descriptor)":""%d"",", \
   json_struct_data->descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 JSON_STRUCT_SNPRINTF( \
   "\"""descriptor""\""":""%d"",", \
   json_struct_data->descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}
Compiler concatenates string literals if nothing stands between them:
"\"descriptor\":%d,"
(\" is a escaped " and part of the string)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 JSON_STRUCT_SNPRINTF( \
   "\"""descriptor""\""":""%d"",", \
   json_struct_data->descriptor)
 {...}
 return json_struct_start_size - json_struct_size;}

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 json_struct_ret = \
   snprintf(json_struct_buf, json_struct_size, \
     "\"""descriptor""\""":""%d"",", \
     json_struct_data->descriptor); \
 JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
   json_struct_size) \
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 {...}
 return json_struct_start_size - json_struct_size;}
We had that before. No need to show it again.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 json_struct_ret = \
   snprintf(json_struct_buf, json_struct_size, \
     "\"""descriptor""\""":""%d"",", \
     json_struct_data->descriptor); \
 JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
   json_struct_size) \
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 {...}
 return json_struct_start_size - json_struct_size;}
Buffer filled with e.g.: "{"\"descriptor\":124}" (of course terminated by \0)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_INT(name) \
        JSON_STRUCT_ELEMENT(name, %d, json_struct_data->name)
# define JSON_STRUCT_ELEMENT(key, template, ...) \
        JSON_STRUCT_SNPRINTF( \
        JSON_STRUCT_QUOT(key)":"#template",", __VA_ARGS__)
# define JSON_STRUCT_QUOT(key) "\""#key"\""
# define JSON_STRUCT_SNPRINTF(...) \
        json_struct_ret = \
        snprintf(json_struct_buf, json_struct_size, \
        __VA_ARGS__); \
        JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
        json_struct_size) \
        /* don't write more characters then size of buffer */ \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */
# define JSON_STRUCT_SIZE_ERROR(ret, size) \
        if (ret >= size) { \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Output buffer in function %s not big enough.\n", \
        __func__); \
        assert(0); \
        }
int json_struct_print_file_descriptor( \
   char* json_struct_buf, \
   size_t json_struct_size, \
   struct file_descriptor *json_struct_data) { \
 char json_struct_hasElements = 0; \
 int json_struct_ret = 0; \
 int json_struct_start_size = json_struct_size; \
 {...}
 json_struct_hasElements = 1; \
 json_struct_ret = \
   snprintf(json_struct_buf, json_struct_size, \
     "\"""descriptor""\""":""%d"",", \
     json_struct_data->descriptor); \
 JSON_STRUCT_SIZE_ERROR(json_struct_ret, \
   json_struct_size) \
 /* don't write more characters then size of buffer */ \
 json_struct_buf += json_struct_ret; \
 /* set pointer to end of written characters */ \
 json_struct_size -= json_struct_ret; \
 /* resize buffer size */
 {...}
 return json_struct_start_size - json_struct_size;}
Function to print the struct file_descriptor as a
json-object to a buffer:
int json_struct_print_file_descriptor(
char* json_struct_buf,
size_t json_struct_size,
struct file_descriptor *json_struct_data)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Again the more complex struct with two elements.
One element a simple variable. The other element
a pointer to one of two possible structs.
We look only on the pointers to other structures

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 JSON_STRUCT_VOID_P_START(file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
We had that before. No need to show it again.
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
At runtime the pointer is either set to NULL or points to a structure.
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Which structure the pointer references to is given
through the enum value. So we can select the
referenced structure at runtime.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_descriptor)
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
Again magic at work: to print the pointed to structure we can use the already
generated function for this structure. Thats because structures can only be elements in other
structures if they are defined before and the definition of all structures in json_structs.h is
transformed by macros to a function.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
To call the print function for the other structure we use as arguments the same buffer
as used for the own structure (via pointer which points to next free byte in buffer), the free size
in that buffer and the other struct to print. As return value we get the written bytes. With that
value we modify the pointer to the next free byte and the free size.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)
We had that before. No need to show it again.
(it’s only another case for struct file_memory)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
 JSON_STRUCT_VOID_P_END(file_type)

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
   default: \
     JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_file_type) \
   } \
   JSON_STRUCT_WRITE(",") \
 }
We don’t know the value that is stored in the enum.
Something went terribly wrong during filling the struct.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
   default: \
     JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_file_type) \
   } \
   JSON_STRUCT_WRITE(",") \
 }
We had that before. No need to show it again.

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
   default: \
     JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_file_type) \
   } \
   JSON_STRUCT_WRITE(",") \
 }

---
#if JSON_STRUCT == JSON_STRUCT_PRINT
# define JSON_STRUCT_VOID_P_START(name) \
        if (NULL != json_struct_data->name) { \
        JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(name)":") \
        switch (json_struct_data->void_p_enum_##name) {
# define JSON_STRUCT_VOID_P_ELEMENT(name, element) \
        case void_p_enum_##name##_##element: \
        json_struct_ret = json_struct_print_##element( \ json_struct_buf, \
        json_struct_size, (struct element*) \
        json_struct_data->name); \
        json_struct_buf += json_struct_ret; \
        /* set pointer to end of written characters */ \
        json_struct_size -= json_struct_ret; \
        /* resize buffer size */ \
        break;
# define JSON_STRUCT_VOID_P_END(name) \
        default: \
        JSON_STRUCT_ENUM_ERROR(json_struct_data->void_p_enum_##name) \
        } \
        JSON_STRUCT_WRITE(",") \
        }
# define JSON_STRUCT_ENUM_ERROR(value) \
        CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
        "Unknown value \"%d\" of enum in function %s.\n", \
        value, __func__); \
        assert(0);
JSON_STRUCT_START(basic)
 JSON_STRUCT_PID_T(process_id)
 if (NULL != json_struct_data->file_type) { \
   json_struct_hasElements = 1; \
   JSON_STRUCT_WRITE(JSON_STRUCT_QUOT(file_type)":") \
   switch (json_struct_data->void_p_enum_file_type)
   case void_p_enum_file_type_file_descriptor: \
     json_struct_ret = \
       json_struct_print_file_descriptor( \
        json_struct_buf, \
        json_struct_size, (struct file_descriptor*) \
        json_struct_data->file_type); \
     json_struct_buf += json_struct_ret; \
     /* set pointer to end of written characters */ \
     json_struct_size -= json_struct_ret; \
     /* resize buffer size */ \
     break;
   JSON_STRUCT_VOID_P_ELEMENT(file_type, file_memory)
   default: \
     CALL_REAL_POSIX_SYNC(fprintf)(stderr, \
       "Unknown value \"%d\" of enum in function %s.\n", \
       json_struct_data->void_p_enum_file_type, __func__); \
     assert(0);
   } \
   JSON_STRUCT_WRITE(",") \
 }
We had that before. No need to show it again.